Fellenbaum Stringed Instruments

105-F Montreat Road

Black Mountain, NC 28711

828-669-5162

tom@acoustic-corner.com

### Mountain Dulcimer Info Sheet

Below you will find information relating to the care of your Mountain Dulcimer.  Please keep this sheet handy for easy reference, as you may need it from time to time.

Strings:

The strings on your mountain dulcimer are standard guitar strings that have ball ends.  These strings are used because they are the easiest to manipulate when having to change or replace strings.  Note how the ball-end of the string seats itself in the groove cut into the tailstock.  You will also notice there are four chrome pins set into the tailstock, these are for attaching loop-end strings.  The loop-end strings are the ones that are commonly found in "sets" of Dulcimer strings.  When using loop-end strings, attach the loops to the chrome pins. Caution: Do not attach ball-end strings to the chrome pins, they are meant for loop-end strings only!  I prefer guitar strings (ball-end) for their ease of replacement and because the wound string (Dulcimer 4th string) is readily available in either Bronze Wound or Phosphor Bronze Wound.  I prefer these Bronze wound strings to the Nickel wound strings that are commonly found in the Dulcimer String sets.

The strings supplied with your dulcimer are the following sizes: 1st and 2nd strings-.012 plain steel; 3rd string-.016 plain steel; 4th string-.026 Phosphor Bronze Wound.  You may vary these string gauges by .001 in either direction without drastically affecting the sound or playability of the instrument.

You will notice that there are two extra grooves cut into both the nut and the bridge.  This is so you may arrange the strings in either the common "double-melody" fashion (which is how your strings were probably arranged when you received your dulcimer) or they can be arranged in the less commonly used "four equal-distant" fashion, where all four strings are equally spaced.

Taking Care of the Finish:

Your dulcimer has been carefully finished with an oil finish. This is a very traditional finish for the Mountain Dulcimer and is one of the more forgiving finishes.  It is not prone to chipping, is easy to repair scratches and leaves the color and texture of the wood to age to a beautiful patina.  The best way to keep the finish looking nice is to handle the instrument carefully, being aware that fingernails, buttons, beltbuckles and any other hard or sharp object can scratch the finish and exposure to water can damage the finish.  I would recommend using lemon oil to renew the finish once a year, or whenever you need to cover up minor dings.  Lemon oil, such as Formby's Lemon Oil Treatment is good for this purpose and is available in many hardware stores and Home Centers. The fretboard is finished with oil and can be cleaned and reoiled once a year by removing all the strings, rubbing the fretboard with a non-abrasive pad (such as those used to clean non-stick cookware) and re-oiling the fretboard with fingerboard oil or lemon oil.  Do not allow the dulcimer to come in contact with the carpet padding that is so often used by dulcimer players to keep the dulcimer from sliding around on the lap.  This material contains solvents that can damage the finish on your instrument!

Any other questions concerning the maintenance of your dulcimer can be directed to me at the above address or telephone number as well as email: tom@acoustic-corner.com

I hope you enjoy your dulcimer,       Your Dulcimer Was Strung With The Following String Gauges:

Tom Fellenbaum                                           ______, ______, ______, ________________